## Slide 1: AD9910
test & Verilog code

## Slide 2: Contents
Evaluation Board Test
Verilog code & python code update for AD9910

## Slide 3
DDS Chip | AD9914 | AD9912 | AD9910
Frequency(bit) | 32 – 64 | 48 | 32
Phase(bit) | 16 | 14 | 16
Amplitude(bit) | 12 | X | 14
DAC(bit) | 12 | 14 | 14
Max Out Freq | 1.2 GHz (1.75 GHz) | 400 MHz | 400 MHz
Max Sys Freq | 3.0 GHz (3.5 GHz) | 1 GHz | 1 GHz
SYNC_IN | O | X | O
 | Parallel & Serial(SPI) | Serial(SPI) | Serial(SPI)

## Slide 4: AD9910
4 mode available
Single ton mode (8 profile)
Ram mode (32 * 1024 RAM)
Parallel mode (real time parameter supply)
DRG mode

## Slide 5: AD9910
4 mode available
Single ton mode (8 profile)
Ram mode (32 * 1024 RAM)
Parallel mode (real time parameter supply)
DRG mode

## Slide 6: AD9910 evaluation board
Tested using modified AD9912 Verilog code
Python code for AD9910 is written

## Slide 7: Modification of AD9912 code
DDS_clock
rcsbar_1
rcsbar_2
rsclk
ja_7
ja_5
ja_4
ja_3
ja_2
ja_0
ja_6
ja_1
rsdio_1
rsdio_2
DDS2_powerdown
DDS1_powerdown
DDS_reset
ck_io_6
ldac_bar
ck_io_39
ck_io_38
ck_io_37
ck_io_36
ck_io_35
ck_io_34
[1:0] DAC_sclk
[1:0] DAC_cs_bar
[1:0] DAC_sdi
DAC_cs_bar[0]
DAC_sclk[0]
DAC_sdi[0]
DAC_cs_bar[1]
DAC_sclk[1]
DAC_sdi[1]
changed to DDS IOUPDATE

## Slide 8
while(1):
print('[1] set_frequency(self, freq, ch1, ch2, unit = \'MHz\')’)
…
order = input('select funct you want to implement')
if( order == '1' ):
freq_in_MHz = float(input('freq_in_MHz : '))
ch1 = int(input('ch1 : '))
ch2 = int(input('ch2 : '))
dds.set_frequency(freq_in_MHz, ch1, ch2)
…
elif( order == '4' ):
freq = float(input('freq : '))
phase = float(input('phase : '))
amplitude = float(input('amplitude : '))
ch1 = int(input('ch1 : '))
ch2 = int(input('ch2 : '))
profile = int(input('profile : '))
dds.set_profile(freq, phase, amplitude, ch1, ch2, profile
= 0, unit_freq = 'MHz', unit_phase = 'FRAC')
elif( order == '5'):
dds.io_update()
elif( order == '6'):
ch1 = int(input('ch1 : '))
ch2 = int(input('ch2 : '))
dds.set_CFR1(ch1, ch2)

## Slide 9: New AD9910 Verilog code
Use Same main FSM
Read & Write is available
4 SPI mode, length of signal can be selected
auto mode available (using FIFO)
Error register added (busy, overrided, overflow, timestamp)
Parallel output available
[7:0]clk_div
cpha
cpol
cspol
[4:0]length
end_spi
slave_en
lsb_first
[7:0]cs
[4:0]dummy
[47:95] dest
[31:0] data
[63:48] dummy
[111:95] dest
[31:0] data
[95:32] timestamp
[127:112] dummy
[11:0] dest
[15:12] dest
functionality
module
SPI configuration
auto mode data
override data

## Slide 10
main FSM
rto_core
fifo
gpo_core
destination check
SPI module
Profile
Parallel
IO update
gpi_core
destination check
rti_core
fifo
[11:0] dest
[15:12] dest

## Slide 11: write process
config_int_list1 = self.set_config(cs = ((ch2 << 1) | (ch1 << 0)),
length = 8)
addr_int_list = self.make_write_list(register_addr << 24)
config_int_list2 = self.set_config( cs = ((ch2 << 1)|(ch1 << 0)), length = 32, end_spi = 1 )
data_int_list = self.make_write_list(register_data)
self.fpga.send_mod_BTF_int_list(config_int_list1)
self.fpga.send_command('WRITE DDS REG')
self.fpga.send_mod_BTF_int_list(addr_int_list)
self.fpga.send_command('WRITE DDS REG')
self.fpga.send_mod_BTF_int_list(config_int_list2)
self.fpga.send_command('WRITE DDS REG')
self.fpga.send_mod_BTF_int_list(data_int_list)
self.fpga.send_command('WRITE DDS REG')

## Slide 12
ja_7
ja_5
ja_3
ja_2
ja_0
ja_6
io[0]
[2:0]DDS1_profile
DDS1_ioupdate
jb_5
jb_7
jb_4
jb_2
[2:0]DDS2_profile
DDS2_ioupdate
jb_3
jc_7
jc_6
jc_5
jc_4
jc_3
jc_2
jc_1
jc_0
jd_7
jd_6
jd_5
jd_4
jd_3
jd_2
jd_1
jd_0
jb_1
jb_0
F[1]
F[0]
[17:0] parallel_out
jb_6
IOBUF
ja_1
ja_4
DDS1_TxEnable
cs2
sck
cs1
IOBUF
io[1]

## Slide 13: Example Code (auto mode)
def exp1():
dds = AD9910(ArtyS7('COM12'))
dds.reset_driver()
dds.auto_mode()
dds.set_profile_register(ch1 = 1, ch2 = 1, freq = 50 * MHz, phase = 0 * RAD,
amplitude = 1.0, profile = 0)
dds.delay_cycle(10000)
dds.set_profile_register(ch1 = 1, ch2 = 1, freq = 100 * MHz, phase = 0 * RAD,
amplitude = 1.0, profile = 1)
dds.delay_cycle(10000)
dds.set_profile_pin(profile1 = 1, profile2 = 0)
dds.auto_start()
UartRx
counter
CSB
reset_driver
set_profile_register
set_profile_register
set_profile_pin
auto_start
10000
20000
0
profile
0
1

## Slide 14: exp1 waveform

## Slide 15: Example Code (auto mode)
def exp2():
dds = AD9910(ArtyS7('COM12'))
dds.reset_driver()
dds.auto_mode()
dds.delay_cycle(500)
dds.set_profile_register(ch1 = 1, ch2 = 1, freq = 50 * MHz, phase = 0 * RAD,
amplitude = 1.0, profile = 0)
dds.set_parallel_amplitude(amplitude = 1.0, parallel_en = 1)
dds.auto_start()
dds.read_exception_log()

## Slide 16: exp2 waveform

## Slide 17: exp2 waveform

## Slide 18: exp2 waveform

## Slide 19: error data
#3 041
0b0010000
0x0000400100000000000001f40004fffc
\r \n
length
error
error data
000…000

## Slide 20: Example Code (override)
def exp3():
dds = AD9910(ArtyS7('COM12'))
dds.reset_driver()
dds.override_enable()
dds.set_profile_register(ch1 = 1, ch2 = 1, freq = 50 * MHz, phase = 0 * RAD,
amplitude = 1.0, profile = 0)
dds.set_profile_register(ch1 = 1, ch2 = 1, freq = 100 * MHz, phase = 0 * RAD,
amplitude = 1.0, profile = 1)
dds.set_profile_pin(profile1 = 1, profile2 = 0)
dds.set_parallel_amplitude(amplitude = 1.0, parallel_en = 1)
dds.initialize(1,1)
dds.read32(1,0,0x00)
dds.read32(0,1,0x01)
dds.read32(1,0,0x02)
dds.read_rti_fifo()
dds.read_rti_fifo()
dds.read_rti_fifo()
dds.read_rti_fifo()
dds.read_rti_fifo()

## Slide 21
spi_core(AD9910_1)
rto_core(rto_core)
counter_matched
[127:0]rto_out
timestamp_error
overflow_error
[31:0]rd_data
full
empty
auto_start
[31:0]wr_data
reset
write
counter
[63:0]counter
cs
read
[4:0]addr
clk
[15:0]dest
SPI_FSM
[127:0]timestamp_error_data
[127:0]overflow_error_data
gpo_core(spi_config)
[63:0]gpo_out
busy
selected
[127:0]error_data
overrided
busy_error
counter_matched
[127:0]gpo_in
[63:0]override_value_input
override_en_input
selected_input
rti_core()
single_spi_output
sck
mosi
miso
sdi
sdo
cspol
cpol
cpha
spi_off
new_in
cs_next
sck_next
cs
slave_en
simple_output(io_update)
simple_output(parallel)
simple_output(profile)
gpi_core
[31:0]din
data_ready
[127:0]gpi_out
read
[31:0]rd_data
[4:0]addr
[63:0]counter
write
cs
[127:0]rti_in
[127:0]timestamp_error_data
write
read
[4:0]addr
[31:0]rd_data
[63:0]counter

## Slide 22
1. wasting resource which is not used many time
and parallel output is not always required
2. need to update fifo in real time
rto_core
FSM
fifo
fifo
rto_core
fifo
rto_core
channel check
channel check
spi_core(AD9910_1)
destination check
mini_gpo_core(AD9910 control)
destination check
mini_gpo_core(Others1)
destination check
fifo
rti_core
mini_gpo_core(Others2)
destination check

## Slide 23: ADC Sampler
8 x BNC
8 x PGIA chip
ADC chip
2 x EEM port
IDC
Sampler Spec
- 8-channel
- 16-bit 1.5MSPS ADC LTC2320-16 ( $48.66 )
- 8 PGIA AD8253 ( $11.36 )
G = 1, 10, 100, 1000
- Basic mode : Sequential input, 700kHz
use single EEM
- Fast mode : Simultaneous input, 1MHz
use dual EEM
- Sample – Urukul Servo mode possible
- USD $1,600

## Slide 24: Sampler – Urukul Servo mode (SUSERVO)
- Use IIR Filter
- DSP is implemented on main processor
- 2 Urukul board per 1 Sampler board