## Slide 1: DDS Debugging
AD9910 Verilog & Board Debug

## Slide 2: Test with Analog Device evaluation board
Profile | Input Frequency | Output Frequency
0 | 100MHz | 50MHz
1 | 120MHz | 60MHz
2 | 140MHz | 70MHz
3 | 160MHz | 80MHz
4 | 180MHz | 90MHz
5 | 200MHz | 100MHz
6 | 220MHz | 110MHz
7 | 240MHz | 120MHz
With IO update signal, there was no glitch problem

## Slide 3: To Fix Noise Problem
Insert attenuator, amplifier
Anlog signal -> high Q
Digital signal -> low Q
Clock length should be more shortened! (long trace -> high L -> high interference)
Digital power, analog ground segmented? -> if not, should be done
Decoupling capacitor should be placed

## Slide 4: Pin
VCC | GND | ja_3 SCLK | ja_2 IOUP2 | ja_1 SDIO2 | ja_0 CSB2
VCC | GND | ja_7 IOUP1 | ja_6 SDIO1 | ja_5 CSB1 | ja_4 PO[18]
VCC | GND | jb_3 P2[1] | jb_2 P2[0] | jb_1 PO[17] | jb_0 PO[16]
VCC | GND | jb_7 P1[2] | jb_6 P1[1] | jb_5 P1[0] | jb_4 P2[2]
GND | PROF1[2] jb_7
GND | PROF1[1] jb_6
GND | PROF1[0] jb_5
GND | IO_UPDATE1 ja_7
GND | IO_UPDATE2
GND | PROF2[0]
GND | PROF2[1]
GND | PROF2[2]
GND | RESET1
GND | SDIO1 ja_6
GND | SCLK1 ja_3
GND | CSB1 ja_5
GND | CSB2
GND | SCLK2
GND | SDIO2
GND | RESET2

## Slide 5: PCB Problem
1. Clock RF circuit does not work properly!
-> impedance due to via, resitor position is not proper
-> S parameter : Spectrum Analyzer, SI : Loop Probe
2. Clock trace and output trace is too close
-> feed through problem occurs
3. Filter can be replaced to IC
4. Digital, analog ground should be separated
5. Decoupling capacitor should be placed to pin more closely
-> Farther decoupling capacitance, more high parasitic inductance.

## Slide 6
Clock Problem

## Slide 7: Reflection

## Slide 8: Reflection

## Slide 9: Termination Design
Terminator Resistor should be placed near the output pin!

## Slide 10: Clock Circuit Problem
Clock source
PCB trace
AD9910 input

## Slide 11: Return Path

## Slide 12: Urukul Termination Design
Termination Resistor is placed near the output pin

## Slide 13: Urukul Termination Design
Termination Resistor is placed near the output pin

## Slide 14: In our AD9910 design
Termination resistor is placed near the input pin->does not work
No termination resistance in output pin
-> high reflection!

## Slide 15: Design Improvement

## Slide 16: In our AD9912 design
PCB trace is not that long(3~5cm) -> RF effect is more lower than case of AD9910
Input resistance difference is lower than case of AD9910
->Reflection is much lower than case of AD9910

## Slide 17: Validation of Clock Trace Problem
Measure return loss(input power - return power) with CAT(Cable and Antenna Test) mode & power on
-> If no reflection : 10 ~ 13dB
Reflection : 0dB
AD9910 board
NA9917A
CLK
PORT

## Slide 18
Trace Position Problem

## Slide 19: AD9910 board
1. Clock trace and output trace is too close
2. Clock trace is too long -> high inductance
-> high interference

## Slide 20: Crosstalk Problem

## Slide 21: Design Improvement
Analog GND
Digital GND
AD9910
Balun
CLK_N
OUTPUT
CLK_P
CLK_N
CLK_N
50
Filter
IC
AD9910
Balun
CLK_N
OUTPUT
CLK_P
CLK_N
CLK_N
50
Filter
IC
Digital Input

## Slide 22
Decoupling Capacitor

## Slide 23: Decoupling Cap Position
Decoupling capacitor should be placed to near the pin of chip
CHIP
CHIP
V

## Slide 24: In Our Case
Decoupling capcacitor is too far from pin